## Slide 1: Introduction to Geospatial Analysis
Key Concepts
Notes: Second day:
MTN (non spatial)
Spatial analysis presentation
Practice with MTN Spatial (I go through)
Practice: have them do other things?

## Slide 2: Spatial Data: Two main types of spatial data are vector data and raster data
Vector Data
Are points, lines, or polygons
Common file formats include shapefiles (.shp) and geojsons (.geojson)
Examples:
  Polygons of countries
  Polylines of roads
  Points of households
Raster Data
Is a spatially referenced grid
Common file format is a geotif (.tif)
For example, satellite imagery comes in a raster format

## Slide 3: Coordinate Reference Systems (CRS)
Coordinate reference systems use pairs of numbers to define a location on the earth
For example, the World Bank is at a latitude of 38.89 and a longitude of -77.04

## Slide 4: Coordinate Reference Systems
There are many different coordinate reference systems, which can be grouped into geographic and projected coordinate reference systems. Geographic systems live on a sphere, while projected systems are “projected” onto a flat surface.
Geographic (Sphere)
Projected (Flat)

## Slide 5: Geographic Coordinate Systems
Units: Defined by latitude and longitude, which measure angles and units are typically in decimal degrees. (Eg, angle is latitude from the equator).
Latitude & Longitude: On a grid X = longitude, Y = latitude.
Sometimes represented as (longitude, latitude).
Also has become convention to report them in alphabetical order: (latitude, longitude) — such as in Google Maps.
Valid range of latitude: -90 to 90
Valid range of longitude: -180 to 180
{Tip} Latitude sounds (and looks!) like latter.

## Slide 6: Geographic Coordinate Systems
Distance on a sphere
At the equator (latitude = 0), a 1 decimal degree longitude distance is about 111km; towards the poles (latitude = -90 or 90), a 1 decimal degree longitude distance converges to 0 km.
We must be careful (ie, use algorithms that account for a spherical earth) to calculate distances! The distance along a sphere is referred to as a great circle distance.

## Slide 7: Geographic Coordinate Systems
Datums
Is the earth flat? No!
Is the earth a sphere? No!
Is the earth a lumpy ellipsoid? Yes!
The earth is a lumpy ellipsoid, a bit flattened at the poles.
A datum is a model of the earth that is used in mapping. One of the most common datums is WGS 84, which is used by the Global Positional System (GPS).
A datum is a reference ellipsoid that approximates the shape of the earth.
Other datums exist, and the latitude and longitude values for a specific location will be different depending on the datum.
Notes: References:
* https://mgimond.github.io/Spatial/chp09_0.html

## Slide 8: Projected Coordinate Systems
Projected coordinate systems project spatial data from a 3D to 2D surface.
Distortions: Projections will distort some combination of distance, area, shape or direction. Different projections can minimize distorting some aspect at the expense of others.
Units: When projected, points are represented as “northings” and “eastings.” Values are often represented in meters, where northings/eastings are the meter distance from some reference point. Consequently, values can be very large!
Click here to see why Toby & CJ are confused (hint: projections!)
Notes: References:
* https://mgimond.github.io/Spatial/chp09_0.html

## Slide 9: Projected Coordinate Systems
Notes: More Funny Things
https://xkcd.com/977/
https://xkcd.com/2489/

## Slide 10: Coordinate Reference Systems
Whenever have spatial data, need to know which coordinate reference system (CRS) the data is in.
You wouldn’t say “I am 5 away”
You would say “I am 5 [miles / kilometers / minutes / hours] away” (units!)
Similarly, a “complete” way to describe location would be: I am at 6.51 latitude, 3.52 longitude using the WGS 84 CRS